Cook book: Samba installation on Linux for "idiots".

Linux version:    6.1
Samba version:    2.0-5a
PC configuration: 350 Mhz K6 CPU with 64Mb of RAM, 20 Gb of harddisk

This documentation describes briefly a step-by-step procedure about
how to install the Samba DOS/Windows file server on a Linux system.
The documentation is based upon the experiences I had when doing
the installation in the LabelCraft office in the period January
10-15 2000.

1)  Get hold of a Linux 6.1 installation disk.

2)  Start the installation by booting from CD. It is also possible
    to make a special Linux Installation boot diskette in Windows,
    but this is not described here. SELECT EXPERT MODE.

3)  Be sure you know all the settings on your network card.
    In my case I used an NE2000 compatible card with IO base 0x2a0, and
    IRQ=10.

4)  When the installation prompts for "Add devices", answer Yes and
    select the proper network card. Also be sure to check the small
    checkbox telling you to set the parameters for the card. Type in
    IO and IRQ (possible DMA also) settings.

5)  DO NOT HAVE ANY SETTINGS FOR DNS AND GATEWAY.
    These settings can easily be added later. Keep things as simple
    as possible.

6)  Select all the modules you want to include in your Linux
    configuration and install Linux.

7)  After the installation is complete, start Linux and log in as "root".

8)  Manually edit the file /etc/hosts.

    When finished, my file looked like this:

    163.17.1.100        LcLinux.localdomain LcLinux SambaLinux
    127.0.0.1           localhost.localdomain localhost SambaLinux

    163.17.1.100 is the IP address of the Linux computer.

    "LcLinux" is the host name of my Linux computer in my network.
    My domain name is set to "localdomain", but it could be changed to
    a "real" domain name like "online.no" at a later stage (using
    LinuxConf and enter the "Config-Networking-Client tasks-Name server
    specification" section).

    "SambaLinux" is an alias name for LcLinux computer. Note that
    this name appears in both lines. IT IS IMPORTANT TO HAVE THREE
    ITEMS ON EVERY LINE, otherwise the "httpd" (Apache Web server
    demon) will fail during startup.

    RESTART THE LINUX COMPUTER.

9)  After Linux has restarted, always log in as "root".

10) Start the "linuxconf" program IN TEXT MODUS. It is more stable
    than the "Gnome" version.

    Start Samba configuration in section "Config-Networking-Server
    tasks-Samba file server". Specify correct work group in the
    section "default", and also specify the disk directories you
    want to share under the "disk shares" section.

    Force Samba to start at boot time.

    This is done in the LinuxConf section "Control-Control
    panel-Control service activity". Click Enter on the Samba line,
    and "enable" it.

    RESTART THE LINUX COMPUTER.

11) Move to a Windows computer and click on the "Network
    neighborhood" icon on the Windows desktop. YOU SHOULD NOW SEE
    YOUR LINUX COMPUTER IN THE LIST. Now stop, you are not finished.

12) Use "LinuxConf" to add the users of the Linux computer. Make
    sure the UserName/ Password matches your Windows UserName password.

13) Go back to your Windows computer, click on "Network
    neighborhood" and click on your Linux computer symbol.

    YOU WILL NOW BE ASKED TO SUPPLY A CORRECT PASSWORD, BUT YOU
    WILL NOT BE ABLE TO LOG IN, BECAUSE LINUX WILL NOT ACCEPT YOUR
    PASSWORD.

    You now have two choices:

    a) Fix-up the Windows registry settings to send uncrypted
       passwords over the network.

       Do this by copying the *.reg files in the
       "/usr/doc/samba-2.0.5a/docs" directory to a DOS floppy disk
       (use "mcopy *.reg a:), and run "regedit <file>.reg" on your
       Windows computer. Make sure you have the correct version for
       your operation system (you will have separate .reg files for
       Windows95, Windows98, Windows NT, and Windows 2000).

    b) Install "Encrypted" passwords in Samba.

       This is the preferred method, because you will then solve
       the Samba password problems once and for all. In the
       documentation below, I assume you have selected this method.

14) Install "Encrypted passwords" in Samba. Follow my "cook book".

    Do the following:

    a) Make the following shell script "sambastart" in "/usr/bin".
       Make sure you have execute rights on the "sambastart" file
       (chmod u+x sambastart):

       /etc/rc.d/init.d/smb start

    b) Make the following shell script "sambastop" in "/usr/bin". Make
       sure you have execute rights on the "sambastop" file
       (chmod u+x sambastop):

       /etc/rc.d/init.d/smb stop

    c) Locate the "encrypt passwords" string in the file
       "/etc/smb.conf" and make sure you have the following lines
       enabled:

       encrypt passwords = yes
       smb passwd file = /usr/local/samba/private/smbpasswd

    d) Make the following shell script "/etc/sambapasswordinit":

       mkdir /usr/local/samba
       mkdir /usr/local/samba/private
       cat /etc/passwd | mksmbpasswd.sh
                                   >/usr/local/samba/private/smbpasswd
       chmod 500 /usr/local/samba/private
       chmod 600 /usr/local/samba/private/smbpasswd

       Make sure the file has execute rights 
       ("chmod u+x /etc/sambapasswordinit").

    e) Type the following commands:

       sambastop
       /etc/sambapasswordinit
       sambastart

    f) Emter the Samba user passwords by using the "smbpasswd"
       program.

       Type "smbpassd" to set the Samba password for "root".
       Type "smbpassd <user>" to set the Samba password for the rest
       of the Linux users you want to have access to the Samba server.

       With "smbpasswd" you can also ADD users (these users will not
       be Linux log-in users), but they will have access to the Samba
       file server. Type "man smbpasswd" for the program options.


    YOU ARE NOW FINISHED.

    Go back to your Windows workstation and try to connect to your
    Samba resources.

    Now you can continue to "play" with the "gateway" and "dns"
    settings on your Linux.

    If it did not work, I wish you good luck.

    If it worked, you will find that the Samba server is a very good
    file server.
 

Ski, Norway, January 15, 2000

Ingar Steinsland
LabelCraft AS